## Slide 1
References
[1] S. Lin et al., "NovelRewrite: node-level parallel AIG rewriting," DAC 2022.
Rethinking AIG Resynthesis
in Parallel
Tianji Liu and Evangeline F.Y. Young
The Chinese University of Hong Kong
Introduction
AIG resynthesis applies different algorithms repeatedly
A commonly used script resyn2 consists of
  rewrite (rw), refactor (rf), (AND-)balance (b)
Previous work of GPU-accelerated rewrite [1]
This work proposes parallel AIG refactor and balance for fully accelerating resyn2
Background
AIG refactoring
  Resynthesis large cones by algebraic factoring
AIG balancing
  Reorder the inputs of AND gates to reduce delay
Parallel Refactoring
Stage 1: identify (M)FFCs covering the AIG
  (M)FFC: a logic cone whose nodes are dedicated to driving the root
  Level-wise parallel from POs to PIs
Theoretical result
  The identified (M)FFCs in stage 1 are disjoint
Parallel Refactoring (cont’d)
Stage 2: resynthesize all local functions in parallel
Stage 3: replace cones in parallel
Parallel Balancing
Stage 1: identify n-input AND gates
  Level-wise parallel from POs to PIs
Stage 2: reconstruct n-input AND gates
  Level-wise parallel from PIs to POs
Results
Comparison with ABC
  rf_resyn: b; rf; rf -z; b; rf -z; b
  Similar or slightly better QoR
Speedup with different AIG sizes
Chart: Avg. Acceleration Ratio over ABC
| b | rf | rf_resyn | resyn2
Acceleration Ratio | 14.8 | 42.7 | 39.5 | 45.9
Summary
14.8x (balance), 42.7x (refactor), 45.9x (resyn2) acceleration over ABC with comparable QoR